## Slide 1: SilverPipelineing
ECE 411 MP3

## Slide 2: Salient Design Aspects
Advanced Features
  8-way set-associative L2 cache
  Victim cache
  Hardware Prefetching (basic)
  One-level dynamic branch prediction (local branch history table)
Tricks to improve performance
  Latched d_mem_rdata and d_mem_address to increase Fmax
  Increased cache line from 128 to 256 bytes

## Slide 3: Quantitative Evaluations
Victim cache
Description of Feature | Competition_1 (ns) | Competition_2 (ns) | Competition_3 (ns) | Final (ns)
3 victim caches | 920,455 | 315,785 | 6,358,425 | 686,365
no victim caches | 927,635 | 319,155 | 6,843,435 | 690,805
Description of Feature | Competition_1 (ns) | Competition_2 (ns) | Competition_3 (ns) | Final (ns)
prefetcher connected to pmem_arbiter | 1,056,410 | 334,000 | 11,202,120 | 803,545
prefetcher connected to L2_arbiter | 1,056,160 | 325,550 | 11,157,770 | 801,100
predictor for prefetcher connected to L2_arbiter | 1,056,159 | 327,110 | 11,157,770 | 801,110
Description of Feature | Competition_1 (ns) | Competition_2 (ns) | Competition_3 (ns) | Final (ns)
no branch prediction | 1,056,159 | 327,110 | 11,157,770 | 801,110
Local branch predictor | 923,205 | 315,935 | 6,399,925 | 689,515
Hardware Prefetcher
Local Branch Prediction

## Slide 4: Things to do Differently
Parameterized Cache
Use performance counters to determine optimum number of lines in victim cache
Improve pseudo LRU implementation
Test different branch predictors

## Slide 5: Thank You